## Slide 2
EE464 HARDWARE PROJECT PRESENTATION
By Emine BOOSTancı
Canberk Kaçan
Erdem Canaz
Erkin Atay Toka
24.04.2024

## Slide 3: Table of Contents
Design Criteria
Topology & Design Selection
Magnetic Design
Simulation Results
Component Selection
Future Work

## Slide 4: 1. Design Criteria
Minimum Input Voltage: 20 V
Maximum Input Voltage: 40 V
Output Voltage: 12 V
Output Power: 60 W
Output Voltage Peak-to-Peak Ripple: 3%
Line Regulation: 3%
Load Regulation: 3%
Isolated Converter
Close Loop Feedback

## Slide 5: 2. Topology & Design Selection
Flyback Converter: low power applications
(up to 100 Watts)
Forward Converter: 50 Watts to a couple of hundred watts
Push Pull Converter: medium power levels (100 Watts to a few kilowatts)
Half and Full Bridge Converter: medium to high power ranges (100 Watts to over 500 Watts)
Push Pull, Half and Full Bridge Convertes are overdesign.

## Slide 6: 2. Topology & Design Selection
Flyback Converter
Forward Converter
No restriction on D
Less components (only transformer)
No resetting the core’s flux
Easiest to design
Leakage inductance
Less efficiency
More ripple and worse regulation
Restriction on D
More components (transformer & inductor)
Resetting the core’s flux
Harder to design
Magnetizing inductance
Higher efficiency
Less ripple and better regulation

## Slide 7: 2. Topology & Design Selection
Single Switch Flyback Converter
Two Switch Flyback Converter
No restriction on D
Simplicity
Snubber Design
Less efficiency
D < 0.5 for CCM
Complexity (high side switch)
High input capacitance
Higher efficiency
Target Efficiency = %80

## Slide 8: 2. Topology & Design Selection
CCM or DCM: CCM. Less ripple but worse core utilization. Analytically easy but nonlineer Bode plot.
Switching Frequency: 90 kHz.
Turns Ratio and Duty Cycle Range: 0.23<D<0.375 N=1

## Slide 9: 3. Magnetic Design
Lm Determination:
=20

## Slide 10: 3. Magnetic Design
Core Selection:
Aim: Operate around 100mT to minimize losses.
Disadvantage: Volume increase. Losses might increase.
Choose ferrite core  less leakage. Fringing fields problem
Higher window area  fill factor auxilary winding
0R45530EC

## Slide 11: 3. Magnetic Design
Core Selection:

## Slide 12: 3. Magnetic Design
Core Selection:
N1=N2=7 turns
lgap=0.7 mm
Bmax=96 mT

## Slide 13: 3. Magnetic Design
Cable Selection:
Choose 2δ (@90kHz 0.44 mm) > Dconductor
AWG 26 ()
Maximum RMS Current is 10A.
For safety take 30 parallel.
From core geometry find MLT and length of the copper.
[1]

## Slide 14: 3. Magnetic Design
Core Losses:
Steinmetz Coefficients
[2]

## Slide 15: 3. Magnetic Design
Experimental Results:

## Slide 16: 4. Simulation Results:Block diagram

## Slide 17
4. Simulation models: Current Feedback

## Slide 18
4. Simulation Results:
20v
3.2w
60v

## Slide 19
4. Simulation Results: Voltage feedback

## Slide 20
4. Simulation Results: Voltage feedback

## Slide 21
4. Simulation Results: Output Filter

## Slide 22
4. Simulation Results: Output Filter

## Slide 23
4. Simulation Results: Auxiliary Supply

## Slide 24
4. Simulation Results: Indicator LEDs

## Slide 25: 4. Simulation Results: Detailed results

## Slide 26: 4. Simulation Results: Summary
Vin = {20, 25, 30, 35, 40}V
Vbat = {11, 12, 13}V

## Slide 27: 4. Simulation Results: Summary
About %75-80 efficiency is expected
The snubber works properly
Output voltage regulation is satisfied

## Slide 28: 5. Component Selection
MOSFET: IRFU3710ZPbF
ID,max ≈ 10A
VDS,max ≈ 65V
 | Parameter | Max. | Units
ID @ TC = 25°C | Continuous Drain Current VGS @ 10V | 56 | A
ID @ TC = 100°C | Continuous Drain Current, VGS @ 10V | 39 | A
VGS | Gate-to-Source Voltage | ± 20 | V
RDS(on) | Drain-to-Source On-Resistance | 18 | mΩ
VGS(th) | Gate Threshold Voltage | 4.0 | V
tr | Rise Time | 43 | ns
tf | Fall Time | 42 | ns
[3]

## Slide 29: 5. Component Selection
Diode: DSA30C100PB (Both for the snubber and the secondary side)
Schottky diode is chosen due to its speed.
Snubber
IF,max ≈ 8A
Vmax ≈ 65V
Secondary Side
IF,max ≈ 9.5A
Vmax ≈ 62V
 | Parameter | Max. | Units
VRRM(TVJ = 25°C) | max. repetitive reverse blocking voltage | 100 | V
VF (IF = 15A, TVJ = 25°C) | forward voltage drop | 0.91 | V
VF (IF = 15A, TVJ = 125°C) | forward voltage drop | 0.73 | V
IFAV (TVJ = 125°C) | average forward current | 15 | A
CJ | junction capacitance | 146 | pF
IR | reverse current, drain current | 250 | µA
[4]

## Slide 30: 5. Component Selection
Output Filter Inductance: SRI1209-100M
Parameter | Max. | Units
L | 10 ± 20% | µH
RDC | 0.03 | Ω
IDC | 10 | A
Test Conditions:
1KHZ / 0.25V
Output
Current
[5]

## Slide 31: 5. Component Selection
Input Capacitor:
4xPKLH-063V471
63V 470µF
Output Capacitor:
4xPKLH-016V471
16V 470µF
Current Sensor IC:
ACS712-30A
Control IC:
UC3845AN
Due to duty cycle limiting behaviour
And various resistors
[6-9]

## Slide 32: 6. Future Work
Optocoupler Design Finalization
Design Implementation on Stripboard
Thermal Analysis
PCB Design (Bonus)
Case Design (Bonus)

## Slide 33: 6. References
[1] W. (n.d.). Round Wire ac Resistance Calculator. https://chemandy.com/calculators/round-wireac-resistance-calculator.htm
[2]“Magnetics - Ferrite Core Loss Calculator.” https://www.mag-inc.com/Design/DesignTools/Ferrite-Core-Loss-Calculator
[3] https://cdn.ozdisan.com/ETicaret_Dosya/652386_243124.pdf [4]https://cdn.ozdisan.com/ETicaret_Dosya/483083_5853486.pdf
[5] https://pdf.direnc.net/upload/10uh-12x12-datasheet.pdf
[6] https://cdn.ozdisan.com/ETicaret_Dosya/465839_6115297.pdf
[7] https://cdn.ozdisan.com/ETicaret_Dosya/342170_703953.pdf
[8] https://pdf.direnc.net/upload/acs712-datasheet.pdf
[9] https://cdn.ozdisan.com/ETicaret_Dosya/501245_5372110.pdf

## Slide 34: In memory of …